## Slide 1: EENG 284 Introduction
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Who are we?
Introduce yourself.

## Slide 4: Lab Objectives
Working with the Quartus IDE
Verilog skills
  Creating logical expressions in Verilog
  Concurrent Signal Assignments
Simulation
  Working with testbenches
  Working with ModelSim (run command)
  Creating timing diagrams
  Verifying design

## Slide 5: Building and testing digital circuits
2 files
  Digital circuit function02.v Logic for circuit
  Testbench function02_tb.v Test inputs for circuit
Notes: Replace <System> with the name of the

## Slide 6: Circuit – code for gates
Concurrent assignment statements
assign p1 = ~a & ~b & c;
assign p2 = ~a & b & ~c;
assign p4 = a & ~b & ~c;
assign p7 = a & b & c;
assign f03 = p1 | p2 | p4 | p7;
All lines of code happen at the same time concurrent
All lines of code happen all the time continuous
Notes: Replace <System> with the name of the

## Slide 7: Testbench – driving inputs to circuit
Notes: Replace <System> with the name of the

## Slide 8: Testbench – instantiation of test circuit
Notes: Replace <System> with the name of the

## Slide 9: Circuit - output
Timing diagram – logic level vs. time
(a,b,c) = (1,1,0) what is f equal? Yes, f is the bottom trace.
Notes: Replace <System> with the name of the