## Slide 1: EENG 284 - Lab 8 simpleDatapath

## Slide 2: Computer basics?
Memory shared between instructions and data
Datapath performs operations
Control unit sequences operations

## Slide 3: Datapath
Instructions stored in instruction register (IR)
Register file has 8 registers, each 16-bits wide – holds program vars
Arithmetic Logic Unit performs 9 different operations
Busses move data around in datapath

## Slide 4: Instructions
I type LDI #value, RD
  I stands for immediate
  Load a constant value into a register
R type ADD RS1, RS2, RD
  R stands for result (from the ALU)
  Performs an operation on a register in the register file
 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I | 0 | 0 | 0 | x | x | immediate |  |  |  |  |  |  |  | dest |  | 
R | 0 | 0 | 1 | fnc |  |  |  | selA |  |  | selB |  |  | selR |  | 

## Slide 5: Deliverables
ALU testbench
Register File testbench
simpleDatapath testbench