## Slide 1: EENG 284 Lab 4
Hi Lo Guessing Game
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
Verilog
  Generics
  LFSR
  Using basic building blocks
    3:8 decoder
    2:1 mux
    Compare
    Mux
    Hex2Seven
Simulation
  Use of Do files
Synthesis

## Slide 3: Game Play
Notes: Replace <System> with the name of the

## Slide 4: System architecture
Design
  Linear Feedback Shift Register
  hiLoWin
Instantiate
  2:1 mux (provided)
  Compare (provided)
  2:4 decoder
  Hex27 (use lab 2 code)
Notes: Talk about the input is transformed into the output using the system architecture

## Slide 5: LFSR
Input
  4-bit vector seed
Output
  4-bit random
Implement
  Use 4 assignment statements
  Shift using bit indices
  Use xor function ^

## Slide 6: 2:1 MUX
Input
  2 N-bit vectors
  1 bit select
Output
  N-bit vector selected
Behavior
  Switches the selected input to the output
Provided Code
// Module definition for the 2:1 mux
module genericMux2x1(y1, y0, sel, f);
// Module instantation for a 2:1 mux in the hiLow digital circuit
genericMux2x1 #(4) muxLsbHex(4'b1111, lsbRandHex, randBut, randLsbSeg);

## Slide 7: Comparator
Input
  2 N-bit vectors
Output
  GT = 1 when X > Y
  LT = 1 when X < Y
  EQ = 1 when X == Y
Behavior
  Switches the selected input to the output
Provided Code

## Slide 8: hiLow Win
Input
  3-bit ones hot
Output
  7-bit segments showing state of play
Implement
  Consider always case statement

## Slide 9: hiLow Module
Glue together
  Module instantiations
  Always/case statements for
    2:4 decoder
    hiLoWin
  Reg types for always/case statement
  Wire for output from instantiations

## Slide 10: Provided Code
Generics
  Generics allow you to specify the width of input signal
  2:1 Mux
  Comparator
Testbench
  hiLow
// Module definition for the 2:1 mux
module genericMux2x1(y1, y0, sel, f);
// Module instantation for a 2:1 mux in the hiLow digital circuit
genericMux2x1 #(7) muxLsbHex(7'b1111111, lsbRandHex, randBut, randLsbSeg);

## Slide 11: Deliverables
LFSR code and testbench for LFSR
Pin assignment
hiLow Testbench output
Working hiLow implementation on Cyclone V GX boards